## Slide 1
Why Symmetric Scales and Hungarian Doesn't
GPU Column-Grouping Strategies for Oblique Apply-Projection
Between 2M×16 and 8M×16 datasets, symmetric’s GPU kernel performance is stable — but hungarian degrades. Why?

## Slide 2
What Each Strategy Does
SYMMETRIC (strategy 6)
• Replace every node’s column indices with a single shared set
• Pick the K most popular columns across all nodes
• Replicate that identical assignment to every row
• Result: 100% column uniformity
• Cost: O(N·K) — independent of dataset row count
HUNGARIAN (strategy 4)
• Reorder each node’s column indices to maximize alignment
• Per iter: remove node → build K×K cost matrix → solve O(K³) Hungarian → reinsert
• 30 iterations × N nodes per iteration
• Result: partial column uniformity (best-effort)
• Cost: O(iters × N × K³) — also independent of row count
Neither strategy’s reordering cost depends on #rows. The difference is what happens in the GPU kernel AFTER reordering.

## Slide 3
The GPU Kernel: It’s Always a Gather
ex_idx = selected_examples[row_start + r]; // monotonic, NOT contiguous dataset_idx = col * num_rows + ex_idx; // column-major layout x = dataset[dataset_idx]; // GATHER — sparse read
• selected_examples per node are sorted (monotonic) but have gaps between indices
• Consecutive threads in a warp hit nearby but NOT adjacent memory addresses
• Each 128-byte cache line (32 floats) may carry only a few useful values
• This is true for BOTH symmetric and hungarian — neither gives contiguous reads
Key insight: the advantage of symmetric is NOT "contiguous reads." It’s about how many DISTINCT columns the L2 cache must hold simultaneously.

## Slide 4
L2 Working Set: 1 Column vs C Columns
SYMMETRIC — Projection slot j
Node 0 ── gather ──▶ column 5 Node 1 ── gather ──▶ column 5 Node 2 ── gather ──▶ column 5 ... ... Node 63 ── gather ──▶ column 5
• All blocks read SAME column
• Cache lines shared across blocks
• L2 footprint = 1 × num_rows × 4B
HUNGARIAN — Projection slot j
Node 0 ── gather ──▶ column 5 │ aligned Node 1 ── gather ──▶ column 5 │ Node 2 ── gather ──▶ column 12 │ mis- Node 3 ── gather ──▶ column 3 │ aligned ... ...
• C distinct columns active at once
• No cross-node L2 reuse between cols
• L2 footprint = C × num_rows × 4B

## Slide 5
Why 8M Breaks Hungarian but Not Symmetric
GPU L2 cache: ~40 MB (A100) / ~50 MB (H100)
Dataset
1 Column
Symmetric (1 col active)
Hungarian (C≈3 cols active)
2M × 16
8 MB
8 MB ✓ fits L2
24 MB ✓ fits L2
8M × 16
32 MB
32 MB ✓ fits L2
96 MB ✗ OVERFLOW
Once L2 overflows:
• Every cache miss on a gather goes to HBM (~10× slower than L2)
• Sparse access amplifies the penalty: each evicted 128-byte cache line carried mostly unused bytes
• Thrashing: column A’s lines evict column B’s, and vice versa — no one stays warm

## Slide 6
Conclusion
• Both strategies produce a sparse gather — neither gives contiguous reads
• The critical difference is L2 working set size:
Symmetric → 1 column per projection slot → scales linearly with row count
Hungarian → C columns per projection slot → scales with C × row count
• At 2M rows: even C > 1 columns fit in L2 → both strategies perform similarly
• At 8M rows: C > 1 columns overflow L2 → hungarian pays HBM latency
on every gather miss, while symmetric still fits
• Symmetric is dataset-size-insensitive because perfect column uniformity
confines the working set to one column’s address range, regardless of size